## Slide 1: Lab VI: Mass Spectrometry-Based Protein Identification and Data Analysis
Mark Dumont
(with assistance and lecture materials from Kyle Swovick, Kevin Welle, and Sina Ghaemmaghami)

## Slide 2
Outline
Determining peptide mass from a family of different mass-to-charge peaks
Isotopes
Mass spectrometry labeling techniques
Data acquisition techniques
Mass spectrometry database searching
Introduction to popular database search programs
Mapping ions to protein/peptide sequences using Protein Prospector
Notes: Today we’ll go over several topics including:
How to determine a peptide’s mass and charge state from mass spec m/z peaks
Natural isotopes and mass spec resolution
Labeling Techniques in mass spectrometry
How to search mass spectrometry data against a protein database
An introduction to several popular database search programs
And then at the end we’ll search your mass spec data using a program called Protein Prospector

## Slide 3
Outline
Determining peptide mass from a family of different mass-to-charge peaks
Isotopes
Mass spectrometry labeling techniques
Data acquisition techniques
Mass spectrometry database searching
Introduction to popular database search programs
Mapping ions to protein/peptide sequences using Protein Prospector

## Slide 4
Protonation of polypeptides in ESI (ElectroSpray Ionization)
Notes: As Dr. Dumont covered Tuesday, all peptides are ionized before entering the mass spec. In protein mass spectrometry, this is most commonly done with ESI. Most commonly, N-termini and basic group side chains become protonated

## Slide 5
Protonation of polypeptides in ESI (ElectroSpray Ionization)
H+
H+
Notes: So in this example, this polypeptide was picked up two protons

## Slide 6
Protonation of polypeptides in ESI (ElectroSpray Ionization)
H+
H+
H+
Notes: But it is also possible for Amide nitrogen to also become protonated so a peptide can actually receive many more protons than just the first two.

## Slide 7
Protonation of polypeptides in ESI
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
Notes: And polypeptides can have a wide range of charge states. For illustrative purposes, we have several lysozyme proteins that we ionize

## Slide 8
Protonation of polypeptides in ESI
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
+1 charge state
H+
Notes: And now we have proteins with no additional protons all the way up to 7 protons and everything in between.

## Slide 9
Protonation of polypeptides in ESI
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
lysozyme
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
H+
+1 charge state
H+
[M]1+
[M]
[M]2+
[M]6+
[M]7+
[M]2+
[M]2+
Notes: From now on, we will denote the number of protons on a peptide as it’s charge state. And can be displayed by M with superscript charge number.
But what does this actually look like on a mass spec readout? As covered already, mass specs just measure mass to charge. And these are all lysozyme so they have the same mass except for each proton added, they gain not only an extra charge, but also extra mass equal to the mass of one hydrogen

## Slide 10
Deconvolution of Multiply charged ions (charge states)
829.4
939.3
991.4
1049.7
1115.3
1189.5
1274.4
1372.4
1486.7
Lysozyme MW: 17,828 Da
Note: Intact, pure, lysozyme gives a family of species
Notes: So the mass spectra for lysozyme would look similar to this. A series of spectra corresponding to a family of charge states

## Slide 11
Deconvolution of Multiply charged ions (charge states)
829.4
939.3
991.4
1049.7
1115.3
1189.5
1274.4
1372.4
1486.7
Lysozyme MW: 17,828 Da
Note: Intact, pure, lysozyme gives a family of species
20+
19+
18+
17+
16+
15+
14+
13+
12+
Notes: And through some math we’ll go through in a little bit, we can assign charge states to each of these peaks.

## Slide 12
Deconvolution of Multiply charged ions (charge states)
829.4
939.3
991.4
1049.7
1115.3
1189.5
1274.4
1372.4
1486.7
Lysozyme MW: 17,828 Da
Note: We don’t get overall charge from mass spec data- only m/z ratios!
20+
19+
18+
17+
16+
15+
14+
13+
12+
Notes: But it’s important to note that we don’t actually get the mass of the peptide from mass spec data; only the mass to charge ratio! So each of these numbers here is the m/z, not the mass.
But we can figure out the mass. Can anyone figure out how we would calculate the mass?

## Slide 13
Deconvolution of Multiply charged ions (charge states)
829.4
939.3
991.4
1049.7
1115.3
1189.5
1274.4
1372.4
1486.7
Lysozyme MW: 17,828 Da
Note: We don’t get overall charge from mass spec data- only m/z ratios!
(m+z)/z
(m+z+1)/(z+1)
(m+z+2)/(z+2)
= 1274.4
= 1372.4
= 1486.7
Notes: Use the formula (m+z)/z = m/z.
And for every additional charge state, we add 1 to z

## Slide 14
Deconvolution of Multiply charged ions (charge states)
829.4
939.3
991.4
1049.7
1115.3
1189.5
1274.4
1372.4
1486.7
Lysozyme MW: 17,828 Da
Note: We don’t get overall charge from mass spec data- only m/z ratios!
(m+z)/z
(m+z+1)/(z+1)
(m+z+2)/(z+2)
= 1274.4
= 1372.4
= 1486.7
Notes: So let’s use this peak here with an m/z of 1372.4

## Slide 15
Deconvolution of Multiply charged ions (charge states)
What is the charge state of the ion with an m/z of 1372.4?
Notes: How do we determine the charge state of this ion?

## Slide 16
Deconvolution of Multiply charged ions (charge states)
What is the charge state of the ion with an m/z of 1372.4?
(m+z+1)/(z+1)
Notes: We use formula (m+z)/z for the least charge ion, and since this ion has one more charge, add one to both the numerator and denominator.
But first we need to find out what m is.

## Slide 17
Deconvolution of Multiply charged ions (charge states)
Notes: So we use the base ion and use m+z/z and set that equal the the m/z mass spec readout. And we solve for m

## Slide 18
Deconvolution of Multiply charged ions (charge states)
Notes: And then we just use some basic algebra to find the value of m

## Slide 19
Deconvolution of Multiply charged ions (charge states)
Substitution
Notes: And then substitute m into the other formula (m+z+1)/(z+1) and solve for z.
And then once we have z, we can easily find m

## Slide 20
Deconvolution of Multiply charged ions (charge states)
829.4
939.3
991.4
1049.7
1115.3
1189.5
1274.4
1372.4
1486.7
Lysozyme MW: 17,828 Da
(m+z)/z
(m+z+1)/(z+1)
(m+z+2)/(z+2)
= 1274.4
= 1372.4
= 1486.7
z = 12
Notes: So now that we have z for the 1372.4 m/z ion, we can measure the actual mass of the ion.

## Slide 21
Deconvolution of Multiply charged ions (charge states)
deconvolution
mass = 17,828 Da
Notes: And deconvolute the entire family of ions into a single mass peak

## Slide 22
Outline
Determining peptide mass from a family of different mass-to-charge peaks
Isotopes
Mass spectrometry labeling techniques
Data acquisition techniques
Mass spectrometry database searching
Introduction to popular database search programs
Mapping ions to protein/peptide sequences using Protein Prospector
Notes: Ok next section we’ll discuss is isotopes and how important resolution is.

## Slide 23
Stable Isotopes
Most elements have more than one stable isotope
  Carbon:
    >98% of atom have a mass of 12 Da (C12)
    1.1% of atoms have an extra neutron (C13)
Element | Mass | Abundance
H | 1.0078 2.0141 | 99.985% 0.015%
C | 12.0000 13.0034 | 98.89% 1.11%
N | 14.0031 15.0001 | 99.64% 0.36%
O | 15.9949 16.9991 17.9992 | 99.76% 0.04% 0.20%
Notes: In nature, most elements exist in more than one stable isotope.
For example, 98% of carbons exist in nature as C12, but a small percentage have an extra neutron and have a mass of 13 daltons.

## Slide 24
Stable Isotopes
Most elements have more than one stable isotope
  Carbon:
    >98% of atom have a mass of 12 Da (C12)
    1.1% of atoms have an extra neutron (C13)
Why does this matter?
Element | Mass | Abundance
H | 1.0078 2.0141 | 99.985% 0.015%
C | 12.0000 13.0034 | 98.89% 1.11%
N | 14.0031 15.0001 | 99.64% 0.36%
O | 15.9949 16.9991 17.9992 | 99.76% 0.04% 0.20%
Notes: But why does any of this matter? Anyone have any thoughts?

## Slide 25
Stable Isotopes
Most elements have more than one stable isotope
  Carbon:
    >98% of atom have a mass of 12 Da (C12)
    1.1% of atoms have an extra neutron (C13)
Why does this matter?
  Mass spectrometers can use these isotopes to determine charge states (z)
Element | Mass | Abundance
H | 1.0078 2.0141 | 99.985% 0.015%
C | 12.0000 13.0034 | 98.89% 1.11%
N | 14.0031 15.0001 | 99.64% 0.36%
O | 15.9949 16.9991 17.9992 | 99.76% 0.04% 0.20%
Notes: We can actually use these isotopes to determine a peptide’s charge state!

## Slide 26
Stable Isotopes for Peptide Analysis
M-R-F-A Peptide
Notes: We’ll use a small peptide to demonstrate this.

## Slide 27
Stable Isotopes for Peptide Analysis
M-R-F-A Peptide
23 Carbons
Notes: This peptide has 23 carbons.
I just said that while 98.8% are C12,

## Slide 28
Stable Isotopes for Peptide Analysis
M-R-F-A Peptide
23 Carbons x 1.1% 13C abundance
Notes: 1.1% of them are going to be C13 so naturally a percentage of the total peptide will have an extra neutron due to C13

## Slide 29
Stable Isotopes for Peptide Analysis
M-R-F-A Peptide
23 Carbons x 1.1% 13C abundance = 0.25 13C per peptide average
  ~25 % of peptides will have one 13C
Notes: And to figure out that percentage, we just multiply 23 by 1.1% to give us 25% of the peptide will have a C13

## Slide 30
Stable Isotopes for Peptide Analysis
M-R-F-A Peptide
23 Carbons x 1.1% 13C abundance = 0.25 13C per peptide average
  ~25 % of peptides will have one 13C
  ~ 6% of peptides will have two 13 C
  … and so on …
Notes: But some peptides will have multiple C13. So we again have a cluster of peaks

## Slide 31
Stable Isotopes for Peptide Analysis
M-R-F-A Peptide
23 Carbons x 1.1% 13C abundance = 0.25 13C per peptide average
  ~25 % of peptides will have one 13C
  ~ 6% of peptides will have two 13 C
  … and so on …
Monoisotopic mass
No 13C atoms
One 13C atom
Two 13C atoms
Three 13C atoms
Notes: With each peak corresponding to different number of neutrons. Starting with 0 C13, or the monoisotopic mass, being the most intense and then every next isotope decreasing in intensity.
We call this entire series of peaks an isotopic envelope.

## Slide 32
Calculating Peptide m/z Values
= 523.2577
+1 Charge State
M-R-F-A Peptide
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
Notes: But remember I said we can use this information to measure charge states and therefore, mass values. So let’s go through figuring out how we can do that.
We know this peptide’s elemental composition

## Slide 33
Calculating Peptide m/z Values
= 523.2577
+1 Charge State
M-R-F-A Peptide
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
Notes: and we know the monoisotopic mass.
We’re gonna have to do some math again. But does anyone have an idea as to what formula we’re going to use?

## Slide 34
Calculating Peptide m/z Values
= 523.2577
+1 Charge State
M-R-F-A Peptide
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
To determine an ion’s m/z:

## Slide 35
Calculating Peptide m/z Values
= 523.2577
+1 Charge State
M-R-F-A Peptide
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
= (m+(z*H+))/z
Notes: So we set the monoisotopic mass equal to that

## Slide 36
Calculating Peptide m/z Values
= 523.2577
+1 Charge State
M-R-F-A Peptide
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
= (523.2577 + (1*1.0073))/1
Notes: And since we already know the charge state, we just plug in all our values

## Slide 37
Calculating Peptide m/z Values
= 523.2577
+1 Charge State
M-R-F-A Peptide
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
= (523.2577 + (1*1.0073))/1
+2 Charge State
M-R-F-A Peptide
= (523.2577 + (2*1.0073))/2
= 523.2577
Notes: But now we have 5the exact same peptide but in the +2 charge state. The elemental composition is exactly the same so the mass is the same, but the charge and monoisotpic m/z are now different. So we can just plug in those different values.
But also, do you notice anything different about these two ions?

## Slide 38
Calculating Peptide m/z Values
In the +1 charge state, isotopes are 1 Da apart
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
In the +2 charge state, isotopes are 0.5 Da apart
+1 Charge State
M-R-F-A Peptide
+2 Charge State
M-R-F-A Peptide
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
Notes: The m/z values are different and the isotopes have different mass differences

## Slide 39
Calculating Peptide m/z Values
In the +1 charge state, isotopes are 1 Da apart
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
In the +2 charge state, isotopes are 0.5 Da apart
+1 Charge State
M-R-F-A Peptide
+2 Charge State
M-R-F-A Peptide
Monoisotopic Mass;
No 13C atoms
One 13C atom
Two 13C atoms
The equation for determining an ion’s charge state is:
Notes: To determine an ion’s charge state, it is simply, 1/the mass delta of the isotopes

## Slide 40
Calculating Peptide m/z Values
Peptide: KEVINWELLE
What is the mass of this peptide?
Notes: So let’s actually do this on a peptide from scratch. We have this peptide here and we want to know it’s mass. How are we gonna go about finding that?

## Slide 41
Calculating Peptide m/z Values
Peptide: KEVINWELLE
What is the mass of this peptide?
Monoisotopic mass = 424.9 m/z
Notes: Take the monoisotopic mass

## Slide 42
Calculating Peptide m/z Values
Peptide: KEVINWELLE
What is the mass of this peptide?
Monoisotopic mass = 424.9 m/z
Mass difference between isotopes = 0.33
Notes: And measure the difference between each isotope

## Slide 43
Calculating Peptide m/z Values
Peptide: KEVINWELLE
What is the mass of this peptide?
Monoisotopic mass = 424.9 m/z
Mass difference between isotopes = 0.33
1/0.33 = Charge State of 3
Notes: This gives us a charge state of 3

## Slide 44
Calculating Peptide m/z Values
Peptide: KEVINWELLE
What is the mass of this peptide?
Monoisotopic mass = 424.9 m/z
Mass difference between isotopes = 0.33
1/0.33 = Charge State of 3
424.9 * 3 = 1274.7
Notes: So then we just substitute z in for the monoisoptic mass and solve for m

## Slide 45
Calculating Peptide m/z Values
Peptide: KEVINWELLE
What is the mass of this peptide?
Monoisotopic mass = 424.9 m/z
Mass difference between isotopes = 0.33
1/0.33 = Charge State of 3
424.9 * 3 = 1274.7
Mass: 1271.7 Da
Notes: But the actual mass of the peptide is 1271.7 Da. Anyone have ideas on how these two values can be different?

## Slide 46
Calculating Peptide m/z Values
Peptide: KEVINWELLE
What is the mass of this peptide?
Monoisotopic mass = 424.9 m/z
Mass difference between isotopes = 0.33
1/0.33 = Charge State of 3
424.9 * 3 = 1274.7
Note: To get the neutral mass, we need to subtract the three protons (charge state was 3)
Mass: 1271.7 Da
Notes: Remember this ion has a +3 charge which means it has 3 protons so the mass is slightly higher within the mass spec. So to get the actual mass, we need to subtract 3 protons.

## Slide 47
Calculating Peptide m/z Values
What is the mass of this peptide?
Monoisotopic mass = 424.9 m/z
Mass difference between isotopes = 0.33
1/0.33 = Charge State of 3
424.9 * 3 = 1274.7
Note: To get the neutral mass, we need to subtract the three protons (charge state was 3)
1274.7 – 3 = 1271.7
Peptide: KEVINWELLE
Mass: 1271.7 Da
Notes: And now our mass match.

## Slide 48
Determining peptide mass from a family of different mass-to-charge peaks
Isotopes
Mass spectrometry labeling techniques
Data acquisition techniques
Mass spectrometry database searching
Introduction to popular database search programs
Mapping ions to protein/peptide sequences using Protein Prospector
Outline
Notes: Ok now that we have some basics, we’ll talk a little about different mass spec methods to label for quantitation

## Slide 49
Metabolic labeling
  Stable Isotopic Labeling by Amino acids in Cell culture (SILAC)
  Stable Isotopic Labeling by Amino acids in Mammals (SILAM)
  Neutron Encoding (NeuCode)
Isobaric labeling
  Tandem Mass Tags (TMT)
  Dimethyl Labeling
  Isobaric Tags for Relative and Absolute Quantitation (iTRAQ)
Mass Spectrometry Labeling Techniques
Notes: In general, there are 2 main types of labeling techniques: metabolic and isobaric. As the name suggests, metabolic labeling happens through labeling amino acids through normal cellular metabolic functions. While isobaric labeling normally occurs after trypsin digestion.

## Slide 50
Metabolic labeling
  Stable Isotopic Labeling by Amino acids in Cell culture (SILAC)
  Stable Isotopic Labeling by Amino acids in Mammals (SILAM)
  Neutron Encoding (NeuCode)
Isobaric labeling
  Tandem Mass Tags (TMT)
  Dimethyl Labeling
  Isobaric Tags for Relative and Absolute Quantitation (iTRAQ)
Mass Spectrometry Labeling Techniques
Notes: The most common form of metabolic labeling is SILAC, or stable isotopic labeling by amino acids I ncell culture (SILAC), but there are slight variations on this idea called SILAM where you label live mice or other mammals, or neucode where the where acids are labeled via neutrons.

## Slide 51
Metabolic labeling
  Stable Isotopic Labeling by Amino acids in Cell culture (SILAC)
  Stable Isotopic Labeling by Amino acids in Mammals (SILAM)
  Neutron Encoding (NeuCode)
Isobaric labeling
  Tandem Mass Tags (TMT)
  Dimethyl Labeling
  Isobaric Tags for Relative and Absolute Quantitation (iTRAQ)
Mass Spectrometry Labeling Techniques
Notes: And for isobaric labeling, by far the most common methodis tandem mass tags, or TMT. But there are also dimethyl labeling and iTRAQ.
But I’ll go a little more in depth on how SILAC and TMT works.

## Slide 52
Metabolic Labeling: Stable Isotopes
Most elements have more than one stable isotope
  Carbon:
    >99% of atom have a mass of 12 Da (C12)
    1.1% of atoms have an extra neutron (C13)
Element | Mass | Abundance
H | 1.0078 2.0141 | 99.985% 0.015%
C | 12.0000 13.0034 | 98.89% 1.11%
N | 14.0031 15.0001 | 99.64% 0.36%
O | 15.9949 16.9991 17.9992 | 99.76% 0.04% 0.20%
Notes: So remember how we talked about a few slides ago that elements naturally exist with some extra neutrons?, which give the ions extra mass? We actually use that phenomenon in SILAC.

## Slide 53
Metabolic Labeling: Relative Quantitation by Isotopic Labeling
Notes: So for example, we have the amino acid arginine. And the monoisotopic would look like this, with no extra neutrons.

## Slide 54
Metabolic Labeling: Relative Quantitation by Isotopic Labeling
Notes: But we can add a neutron to any of the carbons or nitrogens in the arginine. In this example here, every nitrogen is now N15 and every carbon is C13.
Anyone wanna guess what the increase of mass for this arginine would be now?

## Slide 55
Metabolic Labeling: Relative Quantitation by Isotopic Labeling
Notes: This is now 10 daltons heavier so we refer to it as +10. Also it is now heavy arginine while the arginine with no extra neutrons is light arginine.
Anyone wanna guess what the important piece of this is?

## Slide 56
Metabolic Labeling: Relative Quantitation by Isotopic Labeling
(Identical chemistry, different masses)
Notes: That these two amino acids have identical chemistry to each other but have different masses! So these would have the exact same rerention time, charge, etc.
And can anyone predict then what that would look like on a mass spectrum?

## Slide 57
Metabolic Labeling: Relative Quantitation by Isotopic Labeling
(Identical chemistry, different masses)
Notes: They would be in the same spectrum, but because of their different masses, they are separated over the m/z axis. And the height of the peak corresponds to the relative abundance of the both arginines to each other
So can anyone think of reasons this might be helpful?
It allows us to combine two samples with different labels together and compare the relative protein levels between them. And that is called SILAC.

## Slide 58
Metabolic Labeling: SILAC
Notes: So in a traditional SILAC workflow, you have two batches of cell culture. One we are growing in regular media that contains C12 and N14, and the other we are growing in media that contains C13/N15 arginine

## Slide 59
Metabolic Labeling: SILAC
Notes: And then we treat each culture. One with our control treatment, and the other with some sort of miRNA that we hypothesize should change protein expression in some way.

## Slide 60
Metabolic Labeling: SILAC
Notes: And so now all of the proteins that contain arginine will be labeled with either C12/N14 or C13/N15

## Slide 61
Metabolic Labeling: SILAC
Notes: We collect our cells and prepare them for mass spectrometry. We extract protein from our samples, and then before any more downstream steps, we combine them. And then reduce, alkylate, and digest them.

## Slide 62
Metabolic Labeling: SILAC
Notes: And then perform quantitative MS/MS analysis on the combine samples.
So does anyone want to guess as to what some of the benefits might be to this type of technique?
Any downsides?

## Slide 63
Metabolic Labeling: Dynamic SILAC (dSILAC)
Notes: And then perform quantitative MS/MS analysis on the combine samples.
So does anyone want to guess as to what some of the benefits might be to this type of technique?
Any downsides?

## Slide 64
Isobaric Labeling: TMT
Li et al. Nature Methods, 2020
Notes: So isobaric labeling is a little different but it achieves a similar goal. Briefly though, it allows us to combine up to 16 samples together after digestion. In this example here, we have 16 cell culture plates, 8 controls and 8 treatments. We harvest and digest each one, then label them with these 16 tags, combine them all together, then perform LC-MS/MS analysis.

## Slide 65
Isobaric Labeling: TMT
Li et al. Nature Methods, 2020
Notes: And really the reason this is possible is due to the unique structure of the tags. These tags are amine reactive (the purple region) so they will react readily with any amines. Meaning they will bind the N-terminus of peptides.
We’ll discuss in just a little more detail now about what each piece of this means. Each asterisk indicates an atom that has been labeled with a neutron. And the dashed line shows where this tag is cleaved upon fragmentation. So this little group is the red region is cleaved off.

## Slide 66
Isobaric Labeling: TMT
Li et al. Nature Methods, 2020
Notes: And so let’s compare two tags.
These two tags have nearly identical mass, having only a different distribution of neutrons, meaning that as they exist here, they will have the same m/z.
Critically though, in this red region, a carbon is now labeled instead of a neutron. So when fragmentation happens, just this bit at the end is cleaved and now the very slight difference in mass between N15 and C13 can be differentiated .

## Slide 67
Isobaric Labeling: TMT
Li et al. Nature Methods, 2020
Notes: And we do this for up to 16 different combinations

## Slide 68
Isobaric Labeling: TMT
Li et al., Nature Methods, 2020
Rauniyar and Yates, J. Proteome Res., 2014
Notes: So in effect, when we perform LC-MS/MS analysis on these samples, before they are cleaved, the peptides from all 16 samples have the same m/z

## Slide 69
Isobaric Labeling: TMT
Li et al., Nature Methods, 2020
Rauniyar and Yates, J. Proteome Res., 2014
Notes: But upon fragmentation, we now have a series of ions at the low mass range, which are those bits in the red region

## Slide 70
Isobaric Labeling: TMT
Li et al., Nature Methods, 2020
Rauniyar and Yates, J. Proteome Res., 2014
Notes: And if we zoom in closer, we can see that these are actually separated from each other with different intensities. And the intensities can be used as a proxy for the abundance for the peptide in that specific sample. For that reason, these group of ions are referred to as reporter ions.

## Slide 71
Isobaric Labeling: TMT
Low Resolution
Li et al. Nature Methods, 2020
Notes: And

## Slide 72
Isobaric Labeling: TMT
Low Resolution
High Resolution
Li et al. Nature Methods, 2020
Notes: At the mass spec core, we offer a variety of services to fulfill pretty much any mass spec need you might have. We have the capabilities to perform both proteomic and small molecule projects. And we can help with a wide range of services; from helping you design experiments, preparing your samples, assisting with data analysis, writing letters of support, and then helping with both grant writing and publications.
But today, I’m just going to focus on how we use mass spectrometry for proteomics.

## Slide 73
Quantitative Proteomics: Labeling
Labeling Type | Most Common Method | Pros | Cons
Metabolic Labeling |  |  | 
Isobaric Labeling |  |  | 
Notes: Now that we’ve covered some labeling techniques, we’re going to compare them quickly.
Who remember the name of the most common metabolic labeling technique?

## Slide 74
Quantitative Proteomics: Labeling
Labeling Type | Most Common Method | Pros | Cons
Metabolic Labeling | Stable Isotopic Labeling by Amino Acids in Cell Culture (SILAC) |  | 
Isobaric Labeling |  |  | 
Notes: And the most common isobaric labeling method

## Slide 75
Quantitative Proteomics: Labeling
Labeling Type | Most Common Method | Pros | Cons
Metabolic Labeling | Stable Isotopic Labeling by Amino Acids in Cell Culture (SILAC) |  | 
Isobaric Labeling | Tandem Mass Tags (TMT) |  | 
Notes: Can anyone think of some benefits to performing SILAC?

## Slide 76
Quantitative Proteomics: Labeling
Labeling Type | Most Common Method | Pros | Cons
Metabolic Labeling | Stable Isotopic Labeling by Amino Acids in Cell Culture (SILAC) | Samples are combined prior to sample prep | 
 |  | Comparison is performed in the same MS run | 
Isobaric Labeling | Tandem Mass Tags (TMT) |  | 
Notes: What about drawback to this method?

## Slide 77
Quantitative Proteomics: Labeling
Labeling Type | Most Common Method | Pros | Cons
Metabolic Labeling | Stable Isotopic Labeling by Amino Acids in Cell Culture (SILAC) | Samples are combined prior to sample prep | Time-consuming to fully label protein population
 |  | Comparison is performed in the same MS run | Proteome becomes twice as complex
 |  |  | Can be done only with cells that can grow and multiply in media
Isobaric Labeling | Tandem Mass Tags (TMT) |  | 
Notes: Ok benefits for TMT labeling?

## Slide 78
Quantitative Proteomics: Labeling
Labeling Type | Most Common Method | Pros | Cons
Metabolic Labeling | Stable Isotopic Labeling by Amino Acids in Cell Culture (SILAC) | Samples are combined prior to sample prep | Time-consuming to fully label protein population
 |  | Comparison is performed in the same MS run | Proteome becomes twice as complex
 |  |  | Can be done only with cells that can grow and multiply in media
Isobaric Labeling | Tandem Mass Tags (TMT) | Labeling done after digestion (can be performed on nearly any types of sample) | 
 |  | Can combine up to 16 samples together | 
Notes: And drawbacks?

## Slide 79
Quantitative Proteomics: Labeling
Labeling Type | Most Common Method | Pros | Cons
Metabolic Labeling | Stable Isotopic Labeling by Amino Acids in Cell Culture (SILAC) | Samples are combined prior to sample prep | Time-consuming to fully label protein population
 |  | Comparison is performed in the same MS run | Proteome becomes twice as complex
 |  |  | Can be done only with cells that can grow and multiply in media
Isobaric Labeling | Tandem Mass Tags (TMT) | Labeling done after digestion (can be performed on nearly any types of sample) | Tags are expensive
 |  |  | Ratio compression can diminish biological differences
 |  | Can combine up to 18 samples together | High end instrumentation is required to resolve different tags
 |  |  | Samples are combined after digestion
Notes: And drawbacks?

## Slide 80
Determining peptide mass from a family of different mass-to-charge peaks
Isotopes
Mass spectrometry labeling techniques
Data acquisition techniques
Mass spectrometry database searching
Introduction to popular database search programs
Mapping ions to protein/peptide sequences using Protein Prospector
Outline
Notes: Next we’ll discuss different ways that we can acquire our data

## Slide 81
Proteomic Data Acquisition
Two main acquisition methods:
  Data-dependent acquisition (DDA)
    Peptides are isolated for fragmentation and identification
      Selected peptide is primarily due to peptide intensity
  Data-independent acquisition (DIA)
    Entire m/z ranges are fragmented for identification
      m/z ranges are user-defined
Notes: In proteomic experiments, there are two main methods to acquire data: data-dependent and data-independent acquisition

## Slide 82
Proteomic Data Acquisition
Two main acquisition methods:
  Data-dependent acquisition (DDA)
    Peptides are isolated for fragmentation and identification
      Selected peptide is primarily due to peptide intensity
  Data-independent acquisition (DIA)
    Entire m/z ranges are fragmented for identification
      m/z ranges are user-defined
Notes: In a data dependent method, peptides are isolated for fragmentation and identification (it is important to note that in this method, the peptides selected for fragmentation are almost always based on intensity

## Slide 83
Proteomic Data Acquisition
Two main acquisition methods:
  Data-dependent acquisition (DDA)
    Peptides are isolated for fragmentation and identification
      Selected peptide is primarily due to peptide intensity
  Data-independent acquisition (DIA)
    Peptides within wide m/z ranges are fragmented and identified
      m/z ranges are user-defined
Notes: In data independent acquisition, all peptides within a wide m/z range are fragmented and identified. It’s important to note here that these m/z ranges are user-defined.

## Slide 84
Proteomic Data Acquisition: DDA
400
600
800
1000
m/z
0
30
60
90
Relative Intensity
Notes: But to fully grasp how these differ, I feel it’s important to look at spectra. So here’s a fake, fairly simple MS1 spectra

## Slide 85
Proteomic Data Acquisition: DDA
400
600
800
1000
m/z
0
30
60
90
Relative Intensity
571 m/z
MS2 Acquisition Windows
Precursor ion selection window
Notes: In a DDA method, the instrument will isolate and fragment the most intense ion. So here, the mass spec will isolate the ion in the green box at 571 m/z and then fragment that one ion for identification.

## Slide 86
Proteomic Data Acquisition: DDA
400
600
800
1000
m/z
0
30
60
90
Relative Intensity
571 m/z
535 m/z
788 m/z
753 m/z
941 m/z
915 m/z
MS2 Acquisition Windows
Precursor ion selection windows
Notes: And then it will move to less and less intense ions for fragmentation

## Slide 87
Proteomic Data Acquisition: DDA
400
600
800
1000
m/z
0
30
60
90
Relative Intensity
571 m/z
535 m/z
788 m/z
753 m/z
941 m/z
915 m/z
MS2 Acquisition Windows
Precursor ions fragmented:
535 m/z
571 m/z
753 m/z
788 m/z
915 m/z
941 m/z
Notes: And then it will move to less and less intense ions for fragmentation

## Slide 88
Proteomic Data Acquisition: DIA
400
600
800
1000
m/z
0
30
60
90
Relative Intensity
400-500
m/z
400-500
m/z
MS2 Acquisition Windows
Precursor ion selection window
Notes: In a DIA method however, the mass spec isolates peptides just mass on their m/z. So in this example, we have defined the first window as 400-500 m/z. So the mass spec will isolate ALL peptides belonging to that window and fragment them all at the same time and do an MS2 scan.

## Slide 89
Proteomic Data Acquisition: DIA
400
600
800
1000
m/z
0
30
60
90
Relative Intensity
400-500
m/z
500-600
m/z
MS2 Acquisition Windows
Notes: And then we isolate peptides with an mz between 500 and 600

## Slide 90
Proteomic Data Acquisition: DIA
MS2 Acquisition Windows
400
600
800
1000
m/z
0
30
60
90
Relative Intensity
400-500 m/z
500-600
m/z
600-700
m/z
500-600
m/z
500-600
m/z
500-600
m/z
Precursor ion selection windows
Notes: And systemically isolate and fragment ALL the peptides from this spectra.

## Slide 91
Proteomic Data Acquisition: DIA
MS2 Acquisition Windows
400
600
800
1000
m/z
0
30
60
90
Relative Intensity
400-500 m/z
500-600
m/z
600-700
m/z
500-600
m/z
500-600
m/z
500-600
m/z
Precursor ions fragmented:
401 m/z
535 m/z
571 m/z
597 m/z
633 m/z
675 m/z
753 m/z
788 m/z
915 m/z
941 m/z
Notes: And systemically isolate and fragment ALL the peptides from this spectra.

## Slide 92
Full Scan and MS2 Scans
“MS1” Scan
“Full” Scan
“Precursor” Scan
“MS2” Scans
635.3434
Analysis of peptide with m/z = 635.3434
Notes: Now that we have an idea for how a DDA experiment works, let’s look at an actual spectra.
In this MS1 scan, the most intense ion is the one at 635 m/z so the instrument selected it and fragmented it.

## Slide 93
“MS1” Scan
“Full” Scan
“Precursor” Scan
“MS2” Scans
473.8944
Full Scan and MS2 Scans
Analysis of peptide with m/z = 473.8944
Notes: It then isolated and fragmented 473

## Slide 94
“MS1” Scan
“Full” Scan
“Precursor” Scan
“MS2” Scans
849.4437
Full Scan and MS2 Scans
Analysis of peptide with m/z = 635.3434
Notes: And then 849

## Slide 95
“MS1” Scan
“Full” Scan
“Precursor” Scan
“MS2” Scans
Full Scan and MS2 Scans
Notes: And so on until we perform another MS1 scan

## Slide 96
Different MS2 spectra can be collected as a chromatographic peak enters the mass spec

## Slide 98
Proteomic Database Searching
How do we identify peptides from their fragment ions?
Notes: So we have a collection of fragment ions from a DDA method. How do we actually identify peptides and proteins from those?

## Slide 99
Proteomic Database Searching
How do we identify peptides from their fragment ions?
  Using computers, we digest known protein sequences and generate theoretical spectra
    Information we know:
Notes: Using computer software, we can digest known protein sequences and generate theoretical spectra. And this is possible since we have several key pieces of information including:

## Slide 100
Proteomic Database Searching
How do we identify peptides from their fragment ions?
  Using computers, we digest known protein sequences and generate theoretical spectra
    Information we know:
      Where the enzyme cleaves
      The mass of the precursor and fragment ions
      The mass of protein sequences
Notes: Where different enzymes cleave, the mass to charge (and mass) of the precursor and fragment ions, and the masses of various protein sequences

## Slide 101
Proteomic Database Searching
Notes: In an illustrative manner, I’ll demonstrate how this works.
First we have a database with protein sequences.

## Slide 102
Proteomic Database Searching
Notes: We perform an in silico digestion on those sequences using the enzyme we used in our experiment.

## Slide 103
Proteomic Database Searching
Notes: And then for each peptide, we generate theoretical fragment spectra.

## Slide 104
Proteomic Database Searching
Experimentally acquired fragment spectrum
Notes: We take our experimentally acquired spectrum for a mass spectrometer

## Slide 105
Proteomic Database Searching
Experimentally acquired fragment spectrum
Notes: And compare it to each theoretical spectrum and score that comparison

## Slide 106
Proteomic Database Searching
Experimentally acquired fragment spectrum
Notes: If it has a low score, the software rejects that match and moves onto the next comparison

## Slide 107
Proteomic Database Searching
Experimentally acquired fragment spectrum
Notes: Until it finds a match with a high enough similarity score. And the computer says our experimental spectrum confidently matches the theoretical spectrum from fragmenting this peptide sequence.

## Slide 108
Proteomic Database Searching: Random Sequences
Out of hundreds of thousands of peptides, it is reasonable to expect some to randomly match experimental spectra
To combat this, we generate random peptide sequences and compare those matches to experimental spectra
Notes: But it is also a reasonable expectation that out of hundreds of thousands peptides generated, that some of our experimental spectra to just by chance match incorrectly.

## Slide 109
Proteomic Database Searching: Random Sequences
Out of hundreds of thousands of peptides, it is reasonable to expect some to randomly match experimental spectra
To combat this, we generate random peptide sequences and compare those matches to experimental spectra
Notes: To combat this, we match a separate database of random peptide sequences and compare those matches to experimental spectra. So in this example, Our experimental spectrum only has one match to a random sequence so this. And by combining this with probabilistic math, we can calculate confidence scores for every identification that we call false discovery rate (or FDR)

## Slide 110
MS/MS Search Engines: DDA
Name | Lab/Company | Open/Closed-sourced | Free/Paid
MaxQuant | Mann Lab (Munich) | Closed | Free
ProteomeDiscoverer | ThermoFisher Scientific | Closed | Paid
Skyline | MacCoss Lab (Seattle) | Open | Free
Fragpipe | Nesvizhskii Lab (Ann Arbor) | Open | Free
Metamorpheus | Smith Lab (Madison) | Open | Free
Spectronaut | Biognosys | Closed | Paid
ProteinProspector | Burlingame Lab (San Francisco) | Open | Free

## Slide 111
MS/MS Search Engines: DDA
Name | Lab/Company | Open/Closed-sourced | Free/Paid | Benefits
MaxQuant | Mann Lab (Munich) | Closed | Free | Most used proteomic search engine by academic labs Originally designed for SILAC experiments
ProteomeDiscoverer | ThermoFisher Scientific | Closed | Paid | Most used proteomic search engine by core facilities Generates user-friendly excel outputs for data exploration Interactive spectra visualization
Skyline | MacCoss Lab (Seattle) | Open | Free | Allows for the design of custom mass spec experiments Interactive spectra and chromatogram visualization Highly customizable
Fragpipe | Nesvizhskii Lab (Ann Arbor) | Open | Free | Ultra-fast search algorithm Can perform completely open (any database, any cleavage, any modification) Can perform SILAC, TMT, DIA, and IP experiments
Metamorpheus | Smith Lab (Madison) | Open | Free | Ultra-fast search algorithm Can perform completely open (any database, any cleavage, any modification)
Spectronaut | Biognosys | Closed | Paid | Generates user-friendly excel outputs for data exploration Interactive spectra visualization
ProteinProspector | Burlingame Lab (San Francisco) | Open | Free | Can easily modify search parameters Can be performed online

## Slide 112
MS/MS Search Engines: DIA
Name | Lab/Company | Open/Closed-sourced | Free/Paid | Library-Free?
MaxQuant | Mann Lab (Munich) | Closed | Free | Yes
DIA-NN | ThermoFisher Scientific | Semi-open | Paid | Yes
Skyline | Demichev Lab (Zurich) | Open | Free | No
Fragpipe | Nesvizhskii Lab (Ann Arbor) | Open | Free | Yes
EncyclopeDIA | Smith Lab (Madison) | Open | Free | Yes
Spectronaut | Biognosys | Closed | Paid | Yes
Scaffold DIA | Proteome Software | Open | Free | Yes

## Slide 113
What does data from our proteomics core look like?
Notes: And then perform quantitative MS/MS analysis on the combine samples.
So does anyone want to guess as to what some of the benefits might be to this type of technique?
Any downsides?

## Slide 114
Proteomics Core Data: Global Proteomics Quantitation (DIA)
HEK293T cells
4 conditions, 3 replicates per condition
Notes: So back to DIA v DDA, can anyone think of specific reasons or benefits to use one or the other?

## Slide 115
Proteomics Core Data: Global Proteomics Quantitation (DIA)
HEK293T cells
4 conditions, 3 replicates per condition
Notes: So back to DIA v DDA, can anyone think of specific reasons or benefits to use one or the other?

## Slide 116
Proteomics Core Data: Global Proteomics Quantitation (DIA)
HEK293T cells
4 conditions, 3 replicates per condition
And we now have interactive analysis available!
Notes: So back to DIA v DDA, can anyone think of specific reasons or benefits to use one or the other?

## Slide 117
Proteomics Core Data: SILAM-TMT
Hasper et al., Mol. Sys. Biol., 2023
Notes: So back to DIA v DDA, can anyone think of specific reasons or benefits to use one or the other?

## Slide 118
Proteomics Core Data: SILAM-TMT
Hasper et al., Mol. Sys. Biol., 2023
Notes: So back to DIA v DDA, can anyone think of specific reasons or benefits to use one or the other?

## Slide 119
Proteomics Core Data: SILAM-TMT
Hasper et al., Mol. Sys. Biol., 2023
Notes: So back to DIA v DDA, can anyone think of specific reasons or benefits to use one or the other?

## Slide 122
.mgf file from Mass Spectrometer
(fragment of 13,413 MS2 spectra, >500 pages)

## Slide 123
>sp|P0A869|TALA_ECO57 Transaldolase A OS=Escherichia coli O157:H7 GN=talA PE=3 SV=1
MNELDGIKQFTTVVADSGDIESIRHYHPQDATTNPSLLLKAAGLSQYEHLIDDAIAWGKKNGKTQEQQVVAACDKLAVNFGAEILKIVPGRVSTEVDARLSFDKEKSIEKARHLVDLYQQQGVEKSRILIKLASTWEGIRAAEELEKEGINCNLTLLFSFAQARACAEAGVFLISPFVGRIYDWYQARKPMDPYVVEEDPGVKSVRNIYDYYKQHHYETIVMGASFRRTEQILALTGCDRLTIAPNLLKELQEKVSPVVRKLIPPSQTFPRPAPMSEAEFRWEHNQDAMAVEKLSEGIRLFAVDQRKLEDLLAAKL
>sp|P0ADE4|TAMA_ECOLI Translocation and assembly module subunit TamA OS=Escherichia coli (strain K12) GN=tamA PE=1 SV=1
MRYIRQLCCVSLLCLSGSAVAANVRLQVEGLSGQLEKNVRAQLSTIESDEVTPDRRFRARVDDAIREGLKALGYYQPTIEFDLRPPPKKGRQVLIAKVTPGVPVLIGGTDVVLRGGARTDKDYLKLLDTRPAIGTVLNQGDYENFKKSLTSIALRKGYFDSEFTKAQLGIALGLHKAFWDIDYNSGERYRFGHVTFEGSQIRDEYLQNLVPFKEGDEYESKDLAELNRRLSATGWFNSVVVAPQFDKARETKVLPLTGVVSPRTENTIETGVGYSTDVGPRVKATWKKPWMNSYGHSLTTSTSISAPEQTLDFSYKMPLLKNPLEQYYLVQGGFKRTDLNDTESDSTTLVASRYWDLSSGWQRAINLRWSLDHFTQGEITNTTMLFYPGVMISRTRSRGGLMPTWGDSQRYSIDYSNTAWGSDVDFSVFQAQNVWIRTLYDRHRFVTRGTLGWIETGDFDKVPPDLRFFAGGDRSIRGYKYKSIAPKYANGDLKGASKLITGSLEYQYNVTGKWWGAVFVDSGEAVSDIRRSDFKTGTGVGVRWESPVGPIKLDFAVPVADKDEHGLQFYIGLGPEL
>sp|B7L7L9|TAM_ECO55 Trans-aconitate 2-methyltransferase OS=Escherichia coli (strain 55989 / EAEC) GN=tam PE=3 SV=1
MSDWNPSLYLHFAAERSRPAVELLARVPLENIEYVADLGCGPGNSTALLNQRWPAARITGIDSSPAMIAEARSALPDCQFVEADIRNWQPEQALDLIFANASLQWLPDHYELFPHLVSLLNPQGVLAVQMPDNWLEPTHVLMREVAWEQNYPDRGRESLAGIHAYYDILSEAGCEVDIWRTTYYHQMPSHQAIIDWVTATGLRPWLQDLAESEQQLFLTRYHQMLEEQYPLQENGQILLAFPRLFIVARRTE
>sp|Q63450|KCC1A_RAT CamK1 K49E OS=Rattus norvegicus GN=CAMK1 PE=1 SV=2
MLGAVEGPRWKQAEDIRDIYDFRDVLGTGAFSEVILAEDKRTQKLVAIECIAKEALEGKEGSMENEIAVLHKIKHPNIVALDDIYESGGHLYLIMQLVSGGELFDRIVEKGFYTERDASRLIFQVLDAVKYLHDLGIVHRDLKPENLLYYSLDEDSKIMISDFGLSKMEDPGSVLSTACGTPGYVAPEVLAQKPYSKAVDCWSIGVIAYILLCGYPPFYDENDAKLFEQILKAEYEFDSPYWDDISDSAKDFIRHLMEKDPEKRFTCEQALQHPWIAGDTALDKNIHQSVSEQIKKNFAKSKWKQAFNATAVVRHMRKLQLGTSQEGQGQTASHGELLTPVAGGPAAGCCCRDCCVEPGTELSPTLPHQL
>sp|P08515|GST26_SCHJA Glutathione S-transferase class-mu 26 kDa isozyme OS=Schistosoma japonicum OX=6182 PE=1 SV=3
MSPILGYWKIKGLVQPTRLLLEYLEEKYEEHLYERDEGDKWRNKKFELGLEFPNLPYYIDGDVKLTQSMAIIRYIADKHNMLGGCPKERAEISMLEGAVLDIRYGVSRIAYSKDFETLKVDFLSKLPEMLKMFEDRLCHKTYLNGDHVTHPDFMLYDALDVVLYMDPMCLDAFPKLVCFKKRIEAIPQIDKYLKSSKYIAWPLQGWQATFGGGDHPPK
.fasta file: Sequences of all (23,000) E. coli proteins + S. japonicum GST + rat CamKinase
(3166 pages)

## Slide 124
First page after search is completed

## Slide 126
Information on individual proteins identified:
(peptide coverage; individual peptides identified)

## Slide 127
MS2 spectra of individual peptides identified: